## Slide 1: Carbon Intensity of a Transportation Fuel: What Is It and Why Does It Matter?
Kristin Henningson – 5/12/2022

## Slide 2: The Reality of Climate Change
We constantly are bombarded by messages about
What we should do or consume…
What we should stop doing or consuming…
How we can contribute to stopping climate from destroying our way of life…
People have opted for many things, including:
  Not travelling by airplane
  Buying a so-called “zero emissions vehicle”
  Recycling everything at home
  Shopping less at Amazon to avoid vehicle emissions
  Using vegan leather
Notes: With this basis, I’ll be walking through a few concepts to understand the innovation of low-carbon transportation fuels and why they are important to continue providing affordable energy solutions, protecting our way of life and avoiding dependence on foreign powers.

## Slide 3: Audience Poll
Who has heard of the term “Carbon Intensity”?
Who knows what “CO2e” emissions are?
Notes: Level-set audience that most will not know these terms

## Slide 4: What is CO2e?
“Carbon dioxide equivalent”
Can be synonymous with “greenhouse gas emissions”
Total representation of greenhouse gas emissions, on a normalized basis
  Each greenhouse gas has a global warming potential (GWP) that is determined by the regulatory agency
CO2e is the sum of emissions of each greenhouse gas multiplied by its GWP

## Slide 5: What is CO2e?
Gas | Global Warming Potential1
Carbon dioxide (CO2) | 1
Methane (CH4) | 25
Nitrous oxide (N2O) | 298
1From EPA, 40 CFR 98, Table A-1
CO2e
CO2 x 1
N2O x 298
CH4 x 25

## Slide 6: What is CO2e?
CO2e
CO2 x 1
N2O x 298
CH4 x 25
Example: A unit emits 1 pound of CO2, 1 pound of CH4, and 1 pound of N2O
324 lb CO2e
1 lb CO2 x 1
1 lb N2O x 298
1 lb CH4 x 25

## Slide 7: Carbon Intensity of a Transportation Fuel
A calculation of a fuel’s total carbon footprint
  “Life cycle analysis”
“Wells-to-Wheels” analysis
  From feedstock production through end-use of the fuel
Expressed as CO2e emissions per unit of energy in the fuel
CO2e emissions per unit fuel energy
Feedstock Production, Cultivation, Transportation
Production & Distribution of Finished Fuel
End-User Fuel Combustion
Carbon Intensity
Notes: Explain “wells to wheels”
Emphasize per unit of energy in the fuel. Example is two gallons of fuel – each takes same about of CO2e to produce. One has half of the energy – so it has double the CI
Will discuss all of these parts of the process in more detail in upcoming slides

## Slide 8: Carbon Intensity of Various Liquid Transportation Fuels
Ethanol | 
Renewable Diesel | 
Gasoline / Diesel | 
Carbon Intensity (~70 gCO2e/MJ)
Carbon Intensity (~30 gCO2e/MJ)
Carbon Intensity (~100 gCO2e/MJ)
Maximize the benefit if these are a waste!
Notes: Run through each example at a high level. Note and arrows fade in at click!

## Slide 9: Carbon Intensity Variables: Corn Ethanol
Feedstock Production Emissions | Transportation Emissions (Feedstock) | Processing Emissions | Transportation Emissions (Finished Product)
Seeding rate Fertilizer use Fuel use Land-use change Yield rate | Distance by mode of transport | Corn usage rate Electricity use Natural gas use Enzyme use Addition of denaturant | Distance by mode of transport
Co-Products
  Distiller grains
  Corn syrup
  Corn oil
Waste Feedstock
  Using waste fiber with additional enzymes
  Produces “Fiber Ethanol” with a lower CI
Notes: Discuss a few points on this slide, especially if they come up later
Fertilizer
Land use change
Electricity/NG usage
Transportation

## Slide 10: Carbon Intensity Variables: Renewable Diesel
Feedstock Production Emissions | Transportation Emissions (Feedstock) | Processing Emissions | Transportation Emissions (Finished Product)
Farming Oil extraction | Distance, by feedstock, by mode of transport | Feedstock usage rate Electricity use Natural gas use Hydrogen consumption | Distance by mode of transport
Co-Products
  Other renewable hydrocarbons
Waste Feedstocks
  Used cooking oil
  Tallow & Yellow grease
  Produces renewable diesel with even lower CI
Notes: Discuss a few points on this slide
Oil extraction
Hydrogen consumption
Numerous suppliers means large amount of data for transportation

## Slide 11: Carbon Intensity Variables: Fossil Gasoline or Diesel
Feedstock Production Emissions | Processing Emissions | Transportation Emissions
Fuel-burning equipment emissions Leaks to atmosphere | Electricity use Natural gas use Fuel gas combustion Refinery process unit emissions Hydrogen consumption | Raw crude Finished fuel
Co-Products
  Other fossil fuel products
Notes: Discuss a few points on this slide
Crude oil extraction
Refinery process emissions
If asked what the CI is for electric, I will state that I’m not an EV expert, but can speak to liquid fuel CI

## Slide 12: How Can Carbon Intensity Be Lowered?
Example Variable | Example Reduction Opportunity*
Crude oil transportation emissions | Transportation using a renewable source, such as sail boat
Feedstock source | Using a feedstock that is otherwise a waste can provide a large CI reduction
Hydrogen consumption | Use “green” or “blue” hydrogen, rather than “grey”
Electricity or natural gas usage | Replace outdated equipment with more energy-efficient units
Electricity or natural gas usage | Install a renewable power source (solar, wind) at the plant
Process emissions | Carbon capture and sequestration
*Not an exhaustive list. Provided for example purposes only. Not all models will accept these reduction opportunities.
Notes: Discuss a few points on this slide
Sail boat transport - California
Animal fats have a very low CI since they are a waste
CCS will be discussed by Title Sponsor in last slot of day

## Slide 13: What Are We Missing?
Current transportation fuel carbon intensity models do not account for vehicle life cycle
When full vehicle life cycle is included, emissions from EVs are significant from mining raw materials to fabrication to delivery to the showroom
Full Life Cycle Carbon Intensity
Fuel Carbon Intensity
Vehicle Carbon Intensity

## Slide 14: Vehicle Life Cycle
Two times as much CO2 emissions are generated compared to cars fueled by gasoline
Before it leaves the showroom, 12 tons of CO2 emissions have already been generated vs. 6 tons of CO2 emissions from cars fueled by gasoline
2
4
6
8
10
Car Fueled by Gasoline
Battery Electric Vehicle
Embedded CO2 Emissions
(zero miles traveled)
2x higher emissions from mining raw materials to fabrication to delivery
Tons CO 12
2
Mining/Extraction
Power Generation
Fact: Significant Emissions from EV Life Cycle
Manufacturing EVs
Cobalt & Rare Earth Processing

## Slide 15: Vehicle Life Cycle

## Slide 16: Additional Thoughts
Sustainable Aviation Fuel (SAF)
  The same feedstocks used for renewable diesel can be used in sustainable aviation fuel, reducing emissions by ~70%.
  The technology is proven and ready to be implemented.
Electric Vehicles
  Infrastructure build-out is required from current state.
  Potential dependence on foreign powers for 90%+ of the metals needed using current technology.
Online Shopping
  Current solutions exist, where retailers opt for low-carbon fuels, like renewable diesel.
  No need to wait for larger batteries for long-haul or heavy-duty trucks.

## Slide 17: Summary
CO2e = CO2 x GWP + CH4 x GWP + N2O x GWP
Carbon intensity represents CO2e per unit of energy in the fuel, for that fuel’s entire life cycle
Current models do not include vehicle life cycle emissions
A full technology-neutral “apples-to-apples” comparison would model both the vehicle and the fuel carbon intensity

## Slide 18: Questions and Answers